## Slide 1: Fluid Mechanics
Prof. Václav Uruba
uruba@fst.zcu.cz
http://home.zcu.cz/~uruba/vyuka/FM/
UWB FME, KKE
Institute of Thermomechanics ASCR, CTU in Prague FME, CU FFM

## Slide 2: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 3: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 4: Navier-Stokes equation
  Continuity equation
  Momentum equation
  N-S eq. properties, properties of real flows
  Engineering approaches – incompressible, inviscid (Euler e.), extremely viscous (Stokes e.), 2D,…

## Slide 5: Balance equations in fluid mechanics
Mass balance m
Momentum balance h = m . V
Energy balance E
System is open
System
accumulation
me, Ee
min, Ein
mout, Eout
input
output
Time unit
conservation
conservation
Momentum is not conserved – force balance

## Slide 6: Continuity equation
Mass conservation:

## Slide 7: Continuity equation

## Slide 8: Continuity equation
Incompressible fluid
Velocity vector field is for incompressible fluid
divergence-free, SOLENOIDAL

## Slide 9: Newton's laws of motion
Inertia:
Force:
Action and reaction:
1687
Equilibrium of forces: forces on a body are in equilibrium
ANYTIME and Everywhere
A body remains at rest, or in motion at a constant speed in a straight line, unless acted upon by a force.
Inertial system
- no external forces
definition:
Inertial force
If two bodies exert forces on each other, these forces have the same magnitude but opposite directions.
>>> solitary force could not exist !!!
When a body is acted upon by a net force, the body's acceleration multiplied by its mass is equal to the net force.

## Slide 10: Equilibrium of forces
Law of force:
Momentum
Forces acting on elementary volume in space:
Volumetric
Surface

## Slide 11: Equilibrium of forces
direction x:
Cauchy

## Slide 12: Equilibrium of forces
3 comts x:
y:
z:
Tensor (matrix) of deformation rate >>> stress tensor:
Symetrical:
Constitutive relations

## Slide 13: Navier-Stokes equation
Unknown: V(x,t), p(x,t)
Equations: N-S, continuity
3 + 1 = 4
3 + 1 = 4
OK
Laplace operator,
Laplace:

## Slide 14: Interpretation of N-S E
PDE, 1st order in time, 2nd order in space
Non-linear
Non-integrable
Governing parameter: Reynolds number
Representing:
  Equilibrium of forces
  Balance of momentum
Convective
acceleration
Local
acceleration
External
acceleration
Pressure
term
Viscous
term
Reynolds number
Ratio of scales (length- or time-)
Characteristics of convection and diffusion.

## Slide 15: Initial and boundary conditions
Initial conditions:
Boundary conditions:
  Wall :
  IN :
  OUT :
no slip

## Slide 16: No-slip condition

## Slide 17: No-slip condition

## Slide 18: N-S equation
Claude Louis Marie Henri Navier, 1820
Sir George Gabriel Stokes, 1842
Millennium Prize Problems
  Clay Mathematics Institute, Cambridge, Massachusetts
  7 mathematical problems for 3rd millennium, 24.5.2000, Paris
  No.6: Navier–Stokes existence and smoothness
$1 000 000

## Slide 19: Energy equation
First law of thermodynamics
  Heat transfer Q
  Mechanical work W
  Total energy (change) ΔE = Q + W
Ideal (inviscid) gas:
Coefficient of thermal diffusivity,
Temperature conductivity
Coefficient of thermal conductivity
Dissipation function
+ state equation:

## Slide 20: Simplification N-SE
Euler equation
  Inviscid fluid
E.r. of hydrostatics
  Statics
Stokes equation
  Slow motion (creep)
Reynolds equation
  Averaged N-S
o.p.:
Vw,normal = 0
Vw,tangential ≠ 0 !!!
No-slip condition on wall does not hold !!!
Linear !!!
See „Turbulence“

## Slide 21: Euler equation
Viscosity neglected
Appropriate for shock waves modelling
To be added:
  Energy e.
  State e.

## Slide 22: Stokes equation
Very slow flow – „creep“ – small Reynolds number
  Small U: glacier
  Small L: micro-world
  Big ν: honey
Solution with help flow function (potential flow)
Steady – b.c.

## Slide 23: Mathematical modelling
Incompressible case
  Unknown:
    3 velocities
    Pressure
  Equations:
    continuity
    3 momentum
Compressible case
  Unknown:
    3 velocities
    Pressure
    Density
    Temperature
  Equations:
    Continuity
    3 momentum
    Energy
    State
Momentum e.
  Navier-Stokes e.
  Euler e.
  Stokes e.
4
4
6
6

## Slide 24: Stokes flow

## Slide 25: „Normal“ flow

## Slide 26: Thanks for attention

## Slide 27: Continuity equation

## Slide 28: N-S equation

## Slide 29: N-S equation

## Slide 30: Energy equation

## Slide 31: Stress tensor