## Slide 1: Fluid Mechanics
Prof. Václav Uruba
uruba@fst.zcu.cz
http://home.zcu.cz/~uruba/vyuka/FM/
UWB FME, KKE
Institute of Thermomechanics ASCR, CTU in Prague FME, CU FFM

## Slide 2: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 3: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 4: Bernoulli equation
  Derivation from N-SE
  Forms of BE
  Conditions of application, results interpretation
  Examples of BE application: outflow from a vessel, overfall, flow in a pipe

## Slide 5: Daniel Bernoulli
Hydrodynamica (1738)
8.2. 1700, Groningen – 17.3. 1782, Basilej

## Slide 6: Bernoulli equation
N-SE
Fluid
  Incompressible r = const.
  Inviscid n = 0
  Stationary flow
Vector identity
Along streamline:
V
ds
force>>> work(energy) !!!

## Slide 7: Bernoulli equation
Differential e.:
Integration between points „1“ a „2“:
  Pressure energy
  Kinetic energy
  Potential (gravitational) energy
Law of mechanical energy conservation for steady flow of incompressible inviscid fluid in 1-D (along a streamline)
ATTENTION: Navier-Stokes e. is force equilibrium, Bernoulli e. is energy conservation

## Slide 8: Initial presumptions
Incompressible fluid: Ma < 0.3
Inviscid fluid: no shear, effect of walls
Stationary flow: const. b.c. in time, no turbulence
Along a streamline: every streamline different „constant“
No work exhibited: on the streamline there is no pump or turbine
No heat transfer: adiabatic process

## Slide 9: BE validity
Model in a wind tunnel
Tunnel drive
Furnace

## Slide 10: Bernoulli constant
Bernoulli „constant“ H
Substitution:
H is constant in the flow-field:
  Along a streamline
  Along a vortex line
  Everywhere, if
    Flow is vorticity-free
    Vortex lines and streamlines are identical

## Slide 11: BE forms
Energy
Height
Pressure
Static pressure
Total pressure
Hydrostatic pressure
Dynamic pressure

## Slide 12: Hydrodynamic paradoxon

## Slide 13: Hydrodynamic paradoxon

## Slide 14: Applications
Vacuum pump
Carburetor
Sprayer
Wing - lift

## Slide 15: Cavitation
Saturated vapor pressure
  Water, 18°C: pnp = 2 kPa
V > Vcrit, p < pnp
Bubles !!!
boiling
cavitation

## Slide 16: Ideal case
Energy head (Bernoulli)
Hydraulic head
hB
hH

## Slide 17: Reality
ENERGY LOSS
Nominal level of EH
ENERGY LOSS
Reference level

## Slide 18: BE generalization
BE – mechanical energy of a flow
  Potential
  Pressure
  Kinetic
Generalization:
  Internal energy, entalpy
  Transferred heat
  Work
  Friction losses

## Slide 19: Outflow
1: atmosphere patm, V1 = 0
2: outflow patm, V2
3: p3 = (h - l) rg, V3 = 0
4: p4 = patm
5: p5 = patm
Torricelli 1643

## Slide 20: Horizontal outflow
Horizontal outflow
„Vena contracta“
p1 = p2 = p3 = patm
h1 < h2 < h3

## Slide 21: Contraction coefficient

## Slide 22: Outflow from a hole

## Slide 23: Energy balance
Potential energy
Pressure energy
Kinetic energy
Point\Energy | Potential e. | Pressure e. | Kinetic e.
1 | 0 | Big | Small
2 | Small | 0 | Big
3 | Big | 0 | 0

## Slide 24: Velocity, pressure fluctuations
Velocity and dynamic pressure on a streamline:
Reynolds decomposition:
Averaging:
!!!
Pressure and velocity fluctuations:
averaged pressure
does not correspond to
averaged velocity!!!

## Slide 25: Stagnation point
Location on body surface (point, line, curve)
Relative velocity vanishes
Kinetic energy vanishes
Stagnation streamline

## Slide 26: Stagnation point

## Slide 27: Pressures in flowing fluid
Static:
  (3): p3 – h4-3 rg
  (1,2): p1 – h rg = p3 – h3-1 rg
  Total, stagnation:
    (1,2): p2 – H rg
Dynamic:
  (1,2): total - static = 1/2 rV2
Temperature:
  Static
  Total

## Slide 28: Pressures evaluation
Air – gravitational potential energy is neglected:
  pd = p2 – p1 = 1/2rV2
  p3 = p2, p4 = p1
  pd = p3 – p4

## Slide 29: Velocity measurement

## Slide 30: Thanks for attention