## Slide 1: Fluid Mechanics
Prof. Václav Uruba
uruba@fst.zcu.cz
http://home.zcu.cz/~uruba/vyuka/FM/
UWB FME, KKE
Institute of Thermomechanics ASCR, CTU in Prague FME, CU FFM

## Slide 2: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 3: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 4: Flow around bodies
  Forces between surface and flow (pressure, shear)
  Streamlined bodies and bluff bodies
  Forces on a body (drag and lift)
  Flow around cylinder (von Kármán-Bénárd vortex street)
  Theory of thin wing – lift generation

## Slide 5: Boundary layer
Bodies in flow
External aerodynamics
Channels
Internal aerodynamics

## Slide 6: Interaction between a body and flow
Interaction = mutual effect
Body
  Determinates b.c. for flow
Flow
  Generates force on a body – body deformation – b.c. changed
Interaction
  Static – aero(hydro)dynamics
  Dynamical – aero(hydro)elasticity
Feed-back

## Slide 7: Forces exerted on a body
Drag D, FD
  Streamwise
Lift L, FL
  Spanwise (upwards)
Parameters determining the forces
  Geometry
  Viscosity: Re
  Compressibility: Ma
Attention the definition! Re = (UL)/ν
L could be chord or thickness

## Slide 8: Force coefficients
Drag coefficient
Lift coefficient
Dynamics pressure
Area
Pressure force: the coefficients are close to be constant!

## Slide 9: Forces between surface and flow
Friction force
Pressure force (shape)
Drag
Lift
tangential
normal

## Slide 10: Drag
Tvar | Tvarový odpor | Třecí odpor
 | 0% | 100%
 | ∼10% | ∼90%
 | ∼90% | ∼10%
 | 100% | 0%
Streamlined
Body
Bluff
Body
wake
No BL separation
BL separation

## Slide 11: Drag
Body type | Dominant mechanism | CD - Re | FD - U
Streamlined | Friction | CD  1/Re | FD  U
Bluff | Pressure | CD  const. | FD  pd  U2
Chart: Re
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
CDT | 5 | 2.5 | 1.6667 | 1.25 | 1 | 0.83333 | 0.71429 | 0.625 | 0.55556 | 0.5
CDP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: log Re
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
CDT | 5 | 2.5 | 1.6667 | 1.25 | 1 | 0.83333 | 0.71429 | 0.625 | 0.55556 | 0.5
CDP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: U [m/s]
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
FDT | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
FDP | 0.2 | 0.8 | 1.8 | 3.2 | 5 | 7.2 | 9.8 | 12.8 | 16.2 | 20

## Slide 12: Streamlined bodies and bluff bodies – drag
Streamlined body – no BL separation
  Friction force
  Pressure force – small (negligible)
Bluff body – with BL separation
  Friction force - small
  Pressure force - dominant
wake

## Slide 13: Bluff body – cylinder
Inviscid flow
Laminar BL
Turbulent BL
Forces vanish!!!
d’Alambert paradox
Big D
Small D

## Slide 14: Drag 2D bodies
Pozor: log-log graf – přímka je mocninná závislost!

## Slide 15: Drag 3D bodies

## Slide 16: Drag 3D bodies

## Slide 17: Golf ball
23 83 m/s
D = 43-45mm

## Slide 18: Effect of Mach number (compressibility)
Shock waves
Drag increased

## Slide 19: Circular cylinder
D = 0,1m
air
30
m/s
10
m/s
1
m/s
1
mm/s
1
cm/s

## Slide 20: Wing
A = b.c area
A = b/c aspect ratio

## Slide 21: Wing characteristics
A = b/c aspect ratio

## Slide 22: Wing characteristics
Stall

## Slide 23: Theory of lift

## Slide 24: Lift mechanism

## Slide 25: Theory Kutta (1902) – Joukovskii (1906)
2D potential flow – inviscid
+
=
Stagnation point – leading edge
Stagnation point – trailing edge
Drag:
Prandtls theory of BL
d’Alambert
paradox
Lift force
width

## Slide 26: Theory Kutta – Joukovskii
Potential flow
Kutta - Joukovskii
+
=

## Slide 27: Theory Kutta – Joukovskii
Nevazké proudění
Kutta – Žukovskij
Starting
vortex

## Slide 28: Method of vortex panels
Wing profile is simulated by vortices
Used today for wing design, based on Kutta – Joukovskii theory

## Slide 29: New theory on lift
3D Potential flow
+
=
Streamwise vortices – 3D
Johan Hoffman a Claes Johnson, KTH Stokholm
2010

## Slide 30: Laminar flow, low Re
Always 3D!!!

## Slide 31: A 380

## Slide 33: Simulation

## Slide 34: Thanks for attention

## Slide 35: Drag
Krize odporu

## Slide 36: Reynolds number
Re = 1
Re = 100
Re = 100 000
subcritical
Re = 1 000 000
supercritical

## Slide 37: Cylinder in flow
Re = 100 000
subcritical
Re = 1 000 000
supercritical