## Slide 1: Fluid Mechanics
Prof. Václav Uruba
uruba@fst.zcu.cz
http://home.zcu.cz/~uruba/vyuka/FM/
UWB FME, KKE
Institute of Thermomechanics ASCR, CTU in Prague FME, CU FFM

## Slide 2: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 3: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 4: Turbulence
  Properties of turbulence (dynamics, randomness, vorticity, fractality, 3D, effective mixing)
  Turbulence origin (flow stability)
  Equations of turbulent flow RANS
  Solubility of turbulent flows

## Slide 5: Laminar x turbulent flow
Laminar flow of viscous fluid
  Parallel streamlines (movement in layers)
  Spanwise only molecular diffusion
  „Limited“ vorticity
  Stationary (?)
  2D(?)
Turbulent flow
  Non-stationary
  3D
  Vortical
  …
Not potential flow !!!
(internal friction)

## Slide 6: Turbulence – definition (attributes)
Complexity
Randomness (deterministic chaos)
Time-space character
Dynamics (waves)
Topology (3D)
Spectrum of scales (fractality)
Coherent structures
Vorticity (vortices)
Diffusivity
Dissipativity
Irreversibility
Non-linearity
…
Jansen 2000

## Slide 7: Flow in pipe
Water: Recrit ≈ 2000 = > Ucrit ≈ 2 .10-3/D
D [m] | Ucrit [m/s] | Q [m3/s]
0.001 | 2 | 1.6 10-6
0.01 | 0.2 | 1.6 10-5
0.1 | 0.02 | 1.6 10-4
0.5 | 0.004 | 8 10-4
1 | 0.002 | 1.6 10-3
10 | 0.0002 | 1.6 10-2
Laminar
Turbulent
???

## Slide 8: Thermal flow
TURBULENT !!!

## Slide 9: Reynolds experiment
Osborn Reynolds 1883

## Slide 10: Reynolds experiment
Re = 1000
LAMINAR flow
Re = 2000, INTERMITENT flow
Re = 3000
TURBULENT flow

## Slide 11: Stability
stable
indifferent
instable
linearly
instable
non-linearly
System response on perturbance
Potentially instable: SHEAR REGION
Perturbance:
  Turbulence of incoming flow
  Wall roughness
  Wall vibrations
  Wakes behind obstacles
  Thermal perturbances
  Particles in fluid
  Pressure fluctuations (acoustics)
  …
Laminar-turbulence transition promotion
Re

## Slide 12: Shear regions
Basic
  Free SR
  Wall SR (boundary layers)
Combined
  Jet
  Channel
  Wake
Rekrit ≈ 1000
Potentially instable

## Slide 13: Turbulence
Jet in cross flow
Instantaneous snaps
Visualization

## Slide 14: Turbulence
Statistics – time averaged quantities
  Mean
  Variance
Engineering approach

## Slide 15: Reynolds decomposition
Decomposition
  Mean
  Fluctuation
Properties
Ansemble average
Ergodic process: time average

## Slide 16: Averaging properties
Linearity
Commutativity
  with derivative
  With integration
Double averaging
Multiplication averaging
ATTENTION!!!
Time function
Constant

## Slide 17: Velocity and pressure fluctuations
Velocity and dynamic pressure on a streamline:
Reynolds decomposition:
Averaging:
!!!
Averaged dynamic pressure DO NOT correspond to dynamic pressure of mean velocity!!!
Non-linear relation
between pd and V

## Slide 18: Continuity equation
BOTH fields of mean velocities and fluctuations are solenoidal
Operation
averaging
Field of instantaneous velocities is solenoidal
Reynolds:

## Slide 19: Substantial derivative
Operation averaging
?
NELINEÁRNÍ !
Extra term !
Integration per-partés:
= 0 (continuity)

## Slide 20: Reynolds equations
Reynolds 1894
Extra term !
N-S equations
Operation averaging
Reynolds
Eq.
0
Reynolds Averaged Navier Stokes

## Slide 21: Solvability of RANS
Equations: 3 + 1
Unknowns:
3
1
6 (sym)
Total 10 PROBLEM!!!
Additional equations necessary (6)

## Slide 22: Reynolds stress
stress
stress 1
Mean pressure
stress 2
Mean viscous
stress 3
Velocity fluctuations
Reynolds stress
Formal modification

## Slide 23: Reynolds stress
Reynolds stress
Tensor 2nd order
  Symmetric
  Semidefinite
6 independent quantities

## Slide 24: Reynolds stress
Physical meaning
Mean i-momentum flux component generated by velocity fluctuations in j-direction.
Mean j-momentum flux component generated by velocity fluctuations in i-direction.
Always 3D!

## Slide 25: RANS solution
Anisotropic part Rij
Joseph Valentin Boussinesq 1877
Turbulent viscosity hypothesis

## Slide 26: Prandtl mixing length
Estimate
Shear stress
x1
x2
u1
Boundary layer
BL boundary
x1
teff
tturb
x2

## Slide 27: Turbulent viscosity
Property of flow (not fluid)
In turbulence predominates molecular v. (order of magnitude)
Outside turbulence vanishes (approaches 0)
Close to wall (viscose sublayer) vanishes (approaches 0)
Distribution of turbulent viscosity in space:
  Input to solve RANS
  Flow solution
Problem!!!

## Slide 28: Quantities in RANS
  Velocity
  Pressure
  Reynolds stress
  Kinetic energy
  Dissipation rate
  Specific dissipation rate

## Slide 29: Turbulence modelling
Additional equations for Reynolds stress
Algebraical models:
  Mixing length l mix
1-equation models
2-equations models
  Kinetic energy k
  Dissipation rate ε
  Specific dissipation rate ω = ε /k
Equations for Reynolds stresses Rij

## Slide 30: Turbulent flow solution - options
Direct Numerical Simulation – DNS
  Difference equations
Averaged N-S equations – RANS
  Mean values
  Turbulence modelling
Combined approach – URANS, LES (Large Eddy Simulation)
  Big structures – simulation (DNS)
  Small structures – modelling (RANS)
We do note have HW
Basic eng. approach
„Advanced“ eng. approach
More in lectures on mathematical modelling

## Slide 31: Engineering approach
Computer Fluid Dynamics CFD software
  ANSYS
    FLUENT
    CFX
  NUMECA FINE
  OpenFOAM

## Slide 32: Thanks for attention