## Slide 1: Fluid Mechanics
Prof. Václav Uruba
uruba@fst.zcu.cz
http://home.zcu.cz/~uruba/vyuka/FM/
UWB FME, KKE
Institute of Thermomechanics ASCR, CTU in Prague FME, CU FFM

## Slide 2: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 3: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 4: Compressible flow and acoustics
  Compressibility in fluid dynamics (stratified barotropic fluid, compressible flow)
  Shock wave origin, structure
  Compressible flow in practice (subsonic, transonic, hypersonic)
  Basics of acoustics

## Slide 5: Compressibility in FD
Var pressure ⇒ SE ⇒ var density:
Var velocity ⇒ BE ⇒ var pressure:
Var density are „big“ (otherwise could be neglected)
Gas dynamics, „ideal gas“ is considered often

## Slide 6: Fluid dynamics
Continuity equation
Momentum equation (NS, BE)
Energy equation
Equation of state
Incompressible
flow
Compressible flow

## Slide 7: Barotropic fluid
Compressible
Thermodynamics is neglected
ρ = f(p)
Variable density and pressure - quasistatic
Meteorology: isobars = isopyknas
Similar effect: stratification
  Atmosphere (temperature)
  Sea water (salt concentration)
const. pressure
const. density

## Slide 8: Speed of sound
General:
Ideal gas:
Air: c = 331,3 + 0,606 * t m/s
Water: c ≈ 1 500 m/s
M = 0,0289645 kg/mol (molar weight)
R = 8,314510 J (K mol)-1
K: coefficient of stiffness, the isentropic bulk modulus
Air: 1.1 105 Pa
Water: 2.2 109 Pa
Steel: 1.6 1011 Pa

## Slide 9: Mach number
Effect of fluid compressibility
Ernst Mach (1838-1916)

## Slide 10: Sub-, trans-, super-, hypersonic
Subsonic, incompressible: Ma < 0,3
Subsonic compressible: 0,3 < Ma < 1
Transonic: 0,8 < Ma < 1,3 shock waves
Supersonics: 1 < Ma < 3
Hypersonic: 3 < Ma

## Slide 11: Bernoulli equation for compressible flow
BE:
Big velocities, gas – potential e. neglected
Subsonic – isentropic process:
1,4 for 2 atoms ideal gas
Entalpy
Internal energy

## Slide 12: Bernoulli equation for compressible flow
Integration between 1 and 2:

## Slide 13: Bernoulli equation for compressible flow
Point 1: V1 = V, p1 static p
Point 2 is stagnation: V2 = 0, p2 = ptot = p0
Static pressure
Static temperature
Static density

## Slide 14: Bernoulli equation for compressible flow
isoentropic
isoentropic
Non-isoentropic

## Slide 15: Air (isentropic, ideal gas)
g = 1,4
Chart: Ma

## Slide 16: Diffusor x nozzle

## Slide 17: Laval nozzle
1
2
*

## Slide 18: Shock waves
Separate subsonic and supersonic region
Bow SW
Oblique SW
Physical dimensions: thickness bellow 1mm

## Slide 19: Bow shock-wave

## Slide 20: Oblique shock-wave

## Slide 21: Mach cone, angle
Chart: Ma

## Slide 22: Oblique shock-wave
Ma = 2

## Slide 23: Basics of acoustics
Fluctuations:
  Pressure p
  Density r
  Velocity V
Acoustic waves:
  Wave-length l
  Frequency f
  Sound velocity c

## Slide 24: Generation of acoustic waves
Instationarities in flow
Waves
Periodical

## Slide 25: Acoustics in cavities
Resonator: integer multiples of wave-length
  Dead end: node (movement), loop (pressure)
  Free end: node (pressure), loop (movement)

## Slide 26: Supersonic jet - acoustics

## Slide 27: Thanks for attention

## Slide 28: Shock wave
Rankine–Hugoniot