## Slide 1: Fluid Mechanics
Prof. Václav Uruba
uruba@fst.zcu.cz
http://home.zcu.cz/~uruba/vyuka/FM/
UWB FME, KKE
Institute of Thermomechanics ASCR, CTU in Prague FME, CU FFM

## Slide 2: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 3: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 4: Physical modelling
  Theory of similitude, physical modelling
  Measured quantities (pressure, force, velocity, temperature)
  Principles of selected experimental methods (Prandtl probe, hot sensors, optical methods)

## Slide 5: Physical modelling
Similitude
  Geometrical (simplex)
  Physical (complex)
object
model
parametry
výsledky

## Slide 6: Physical dimensions system
SI system - 7 basic physical units:
  Kilogram
  Meter
  Candela
  Second
  Ampere
  Kelvin
  Mole
FM
SI: International System of Units

## Slide 7: Buckingham Theorem
Relevant quantities q1 - qn
Simplex pi = qj/qk
Complex pi = q1b1 . q2b2 . …. . qnbn
n physical quantities q1,…,qn
  Model: f(q1,…,qn) = 0
k basic physical units
p = n – k dimensionless parameters complex π1,…,πp
  Model: F(π1,…,πp) = 0
  + simplex Pi

## Slide 8: Buckingham theorem
No need for mathematical model
Only “relevant” quantities
BT suggests methods
Dimensional matrix
Ambiguous solution – choice, physical meaning

## Slide 9: Dimensionless parameters in fluid mechanics
Reynolds number
Mach number
Strouhal number
Force coefficients
Convection
Diffusion
Compressibility effect
Dimensionless frequency
Dimensionless force

## Slide 10: Example: sphere in flow
Relevant quantities: F[kg.m/s2], V[m/s], d[m], ρ[kg/m3], n[m/s2] F = f(V,d,ρ,ν)
n = 5, k = 3, p = 2
Dimensionless parameters:
CD
Re
[m], [kg], [s]

## Slide 11: Measured quantities
Pressure
Temperature
Speed
Force
Material parameters
  Density
  Viscosity
  …
State quantities
Functions of the state quantities
Value
  Static
  Total
  Dynamic

## Slide 12: Pressures measurement
Pressure
  Static
  Total
  Dynamic
Probe: Pitot-static
(Prandtl)
Directional probe
Static pressure on wall

## Slide 13: Pressures measurement
Manometers
  Liquid
  Bourdon tubes
  Bellows
  Membranes

## Slide 14: Temperature measurement
Temperature
  Static
  Total
  Recovery
Thermometers
  Expansivity
  Thermocouple
  Resistance (Pt)
  Thermistors (semiconductors)
  Liquid crystals
  IR
Measures surface temperature and not the fluid !!!

## Slide 15: Speed measurement
Pressures
Hot sensors
Optical methods
  LDA
  PIV
The only 2D method
Point methods

## Slide 16: Speed from pressures
Pressure
  Static
  Total
  Dynamic
Bernoulli equation

## Slide 17: Hot sensors
Hot wire or film
Sensor is cooled: gas (thermal properties), temperature, speed
Measuring point:
The only method for frequency above 10kHz (up to 200kHz)

## Slide 18: Constant Temperature Anemometry – CTA
Wire W, Pt dia 1-10 μm
Film on glass, Ni, Pt thickness 0,5-1 μm

## Slide 19: Directional sensitivity

## Slide 20: Orientation ambiguity

## Slide 21: Probes

## Slide 22: Calibration
Nastavení podle tlaků
Cooling law

## Slide 23: Hot sensors anemometry
Malý měřicí bod
Dobrá citlivost
Vysoká přesnost (závisí na kalibraci)
Vysoké pfrekvence
Rozsah rychlostí (vzduch: 0.1m/s – 5M)
Citlivost k dalším veličinám (T, p, složení)
Intrusivní metoda
Choulostivá sonda
Problémy v průmyslovém prostředí
Nejistota v orientaci rychlosti
Je třeba kalibrace
Citlivost k dalším veličinám (T, p, složení)

## Slide 24: Optical methods
Particles
  Kapičky oleje
  TiO2, MnO
  Polyamid
Částice by měly „kopírovat“ chování tekutiny
Ideal: same density
Methods:
  Laser Doppler Anemometry – LDA
  Particle Image Anemometry – PIV

## Slide 25: Laser Doppler Anemometry – LDA

## Slide 26: LDA system

## Slide 27: Application examples

## Slide 28: LDA
High accuracy
No calibration needed
Not intrusive
Up to 3 velocity components
Small measuring point
Velocity orientation
Particles needed
Uneven sampling
Expensive

## Slide 29: Particle Image Velocimetry – PIV
Measurement in 2D (3D) – space correlations

## Slide 30: Velocity evaluation

## Slide 31: Snap A

## Slide 32: Snap B

## Slide 33: Snap

## Slide 34: Vector field

## Slide 35: Vectors + vorticity

## Slide 36: PIV
Space correlations
No calibration
Not intrusive
2 or 3 velocity components
Velocity orientation
Particles are needed
Lower accuracy
Expensive

## Slide 37: Experimental facilities
Wind tunnels
Water facility
Shock tubes (hypersonic)

## Slide 38: Wind tunnel
Open
Close-circuit

## Slide 39: UWB flow-down facility

## Slide 40: Garman-Duch tunnel (Marknesse)

## Slide 41: Thanks for attention