## Slide 1: Fluid Mechanics
Prof. Václav Uruba
uruba@fst.zcu.cz
http://home.zcu.cz/~uruba/vyuka/FM/
UWB FME, KKE
Institute of Thermomechanics ASCR, CTU in Prague FME, CU FFM

## Slide 2: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 3: Fluid Mechanics - lectures
Introduction, concepts, definitions
Statics
Kinematics
Dynamics
Bernoulli equation
Shear regions
External flows
Internal flows
Flow machines
Turbulence
Compressible flows and acoustics
Physical modelling
Mathematical modelling

## Slide 4: Mathematical modelling of flow
  Simulation of laminar and turbulent flow
  Engineering methods (RANS, LES)
  Validation x verification
  Examples, software, results interpretation

## Slide 5: Problem definition
Boundary conditions
Initial conditions (nonstationary)
Fluid properties
  „Material“ properties (density, viscosity, heat conductivity,…)
Flow properties
  Topology (1D, 2D, 3D)
  Laminar x Turbulent, transitional
Simplifications
Mathematic model choice
  N-S E, Euler E., Stokes E., Bernoulli E.

## Slide 6: Solution strategy
Physical problem PP definition
Simplifications
Definition of simplified problem (only selected physical aspects considered) – mathematical model MM
Solution of simplified problem
Validation (code)
Verification MM
Result transfer from MM towards PP

## Slide 7: Simplifications – MM design
Geometry
  3D – PP always!
  2D plain geometry
    Plain b.c.
    Border effect neglected (important?)
    Only statistics, instantaneous is 3D!
    Often physically instable
  1D solution „on streamline“, 1. (0.) approx. - BE
Fluid properties
  Compressibility
    Incompressible, Ma < 0.3, ρ = const., no thermodynamics
    compressible: energy e.!
  Viscosity
    Inviscid, compressible
Reality:
3D
Compressible
Viscous
Turbulent (mostly)
Incompressible and inviscid model
no relevant physical information!
Integral balance estimate
(flow rate, force,…)

## Slide 8: Mathematical models
3D geometry
Dynamics (nonstationary) 3D
Turbulence
Shear regions, boundary layers
Friction forces, pressure forces (wake)
Shock waves
Acoustics
Thermodynamics
3D MM
Viscous MM
Compressible MM
Physical problem PP

## Slide 9: Dimension 3D
3D
  Whole region
  Part region (symmetry)

## Slide 10: Dimension 2D - plain

## Slide 11: Cylinder in cross-flow
2D
3D

## Slide 12: Dimension 2D - rotational symmetry
Statistics 2D
Dynamics 3D

## Slide 13: Discretization
In space
In time
Link! (Courant–Friedrichs–Lewy condition - CFL)
velocity
1D:
2D:
general:

## Slide 14: Real simulation

## Slide 15: Turbulent flow solution options
Direct Numerical Simulation of N-S E – DNS
  Difference eq.
Averaged N-S E – RANS
  Mean values
  Turbulence modelling
Combined approaches – URANS, LES
  Big structures – simulation (DNS)
  Small structures – modelling (RANS)
We have not sufficient resources
Basic engineering approach
„Advanced“ engineering approach
CFD – Computer Fluid Dynamics
DNS: Direct Numerical Simulation
N-S: Navier-Stokes
RANS: Reynolds Averaged Navier-Stokes
URANS: Unsteady RANS
LES: Large Eddy Simulation

## Slide 16: Mathematical modelling in a point
DNS
RANS
LES

## Slide 17: Mathematical modelling BFS
BFS – Backward Facing Step

## Slide 18: Mathematical modelling BFS

## Slide 19: Mathematical modelling BFS

## Slide 20: Mathematical modelling BFS

## Slide 21: Mathematical modelling
Reality: real physical process, physical object and conditions
Conception model: all equations including b.c. and i.c. (PDE)
Computational model: implementation of CM into computer system (numeric)
Conception
model
Reality
Computational
model
Kvalifikation
Verifikation
Validation
Programming
Simulation
Analysis
objekts - processes - methods
Team work!!!:
physicians, theoreticians, experimentalists, mathematicians, programmers

## Slide 22: Validation x Verification
Validation
  Experiment – comparison in suitable locations
Verification
  Discretization, no. of elements, distribution (density)
  Type of elements (structured, unstructured, …)
  Order of numerical scheme
PHYSICS
MATHEMATICS

## Slide 23: Practical solutions
Computer Fluid Dynamics CFD software
  ANSYS
    FLUENT
    CFX
  NUMECA FINE
  OpenFOAM

## Slide 24: Computers power
Today:
  PC: RANS, simple LES
  Supercomputers: LES, trivial DNS

## Slide 25: Thanks for attention