## Slide 1: Test

## Slide 2: In the Navier-Stokes equation for an incompressible fluid the following unknowns are present
3 velocity components only
pressure and 3 velocity components
pressure, density and 3 velocity components
pressure and density only

## Slide 3: Turbulent viscosity is a property of
flow, it is constant in the flow region
flow in the given point
fluid, it is constant in the flow region
fluid in the given point

## Slide 4: Euler equation describes motion of the
incompressible viscous fluid
compressible viscous fluid
inviscid fluid
gas only

## Slide 5: Continuity equation holds
only for incompressible fluids
only for inviscid fluids
only for gases
for any fluid

## Slide 6: Turbulence could be born
in still (not flowing) fluid
in a shear region
in a free flow
close to wall only

## Slide 7: Navier-Stokes equation formulates
momentum conservation
momentum balance
moment balance
forces equilibrium

## Slide 8: Reynolds equations for an incompressible fluid could be solved
directly, no additional information is needed
only if additional information on fluctuations is added
only continuity equation should be added
energy equation should be added

## Slide 9: Operation of averaging is
linear operation
quadratic operation
cubic operation
exponential operation

## Slide 10: Boundary condition on a non-permeable wall for the NS equation:
pressure is zero
velocity component perpendicular to the wall is zero
velocity component parallel to the wall is zero
velocity vector is equal to one

## Slide 11: To solve Reynolds equations (RANS) the following could NOT be defined
initial conditions
boundary conditions
turbulence model
continuity condition

## Slide 12: Reynolds equations are the
continuity equations for turbulent flow
averaged Navier-Stokes equations
turbulence model
equations describing the laminar flow

## Slide 13: For functions of time and averaging operation is NOT valid:
mean value of product is equal to product of mean values
mean value of sum is equal to sum of mean values
mean of integral is equal to integral of mean values
mean of derivative is derivative of mean values

## Slide 14: Growing amplitude of perturbances has the following effect on the laminar-turbulent transition
speed-up in time
speed-up in space
speed-down in time
speed-down in space

## Slide 15: Stokes equation describes motion of the
incompressible inviscid fluid
compressible inviscid fluid
viscid fluid
gas only

## Slide 16: For flow of inviscid fluid the Reynolds number approaching
0
1
1 million
Infinity

## Slide 17: In the Navier-Stokes equation for a compressible fluid the following unknowns are present
3 velocity components only
pressure and 3 velocity components
pressure, density and 3 velocity components
pressure and density only

## Slide 18: Laminar flow is the flow of
inviscid fluid
always nonstationary
always swirling
viscous fluid in layers

## Slide 19: Reynolds stress is from the mathematical point of view
scalar
vector
antisymmetric matrix
symmetric matrix

## Slide 20: Stability analysis examines
disturbances growth in a turbulent flow
disturbances growth in a laminar flow
disturbances propagation in a turbulent flow
disturbances propagation in a laminar flow

## Slide 21: For solution NSE for incompressible fluid is NOT necessary
initial conditions
boundary conditions
turbulence model
continuity condition

## Slide 22: Reynolds decomposition is
decomposition of pressures to static and dynamic
decomposition of velocities into directions
decomposition of pressures and velocities to mean and fluctuating components
decomposition of pressures and velocities into elements

## Slide 23: Reynolds stress is an additional stress caused by
mean velocities
fluctuating velocities
mean pressure
fluctuating pressure

## Slide 24: Types of shear zones:
free shear zone
coupled shear zone
wall shear zone
inviscid shear zone

## Slide 25: Initial perturbance growing law in the instable laminar flow is
linear
power
exponential
logarithmic